MOVing Data: The Case of -1

---
How to do load X0 with -1?
1. Let’s recall last time, we could load X0 or W0 with a small integer, e.g., using MOV X0, #3.
3. This appeared in our listing as 0x060080D2, or
4. 0xD2800060 in readable order because ARM is little Endian.
6. This operation had an imm16 field, in which we placed 0b0000000000000011 or 0x03.

---
How to do load X0 with -1?
1. But -1 represented as a 64 bit integer is
2. 0xFFFFFFFFFFFFFFFF (bit pattern of all 1s)
  We can’t fit this into a 16 bit immediate field.
4. Let’s see what GCC does with an example:
  1. int main(void){
  2. long int num = -1;
  3. return 0;
  4. }

---
How to do load X0 with -1?
1. Running GCC to assembly source produces
  1. main:
  2. sub	sp, sp, #16
  3. mov	x0, -1
  4. str	x0, [sp, 8]
  5. mov	w0, 0
  6. add	sp, sp, 16
  7. ret

---
How to do load X0 with -1?
1. But the assembly source is misleading here. Let’s look at the listing file:
  1. 7 main:
  2. 8	0000	FF4300D1	sub	sp, sp, #16
  3. 9	0004	00008092	mov	x0, -1
  4. 10	0008	E00700F9	str	x0, [sp, 8]
  5. 11	000c	00008052	mov	w0, 0
  6. 12	0010	FF430091	add	sp, sp, 16
  7. 13	0014	C0035FD6	ret

---
How to do load X0 with -1?
1. Let’s decode this, since the op code appears different (D2 vs. 92).
3. Re-ordered, the instruction is 0x92800000.
5. If we look at the Aarch64 instruction spreadsheet, we find that this corresponds not to MOV, but rather MOVN. What’s the difference?

---
MOV vs MOVN: N is for NOT
MOVN has similar syntax to MOV. It has:
- sf: 1 bit, 0 for 32 bit or 1 for 64 bit
- op code: 00100101
- hw: 2 bits, used for shifting (leave 00 for now)
- imm16: 16 bit integer, 0 through 65535
- Rd: 5 bits, register number
1. imm16 is a bit pattern of our choosing, which in our example was 0x0000.

---
MOV vs MOVN: N is for NOT
imm16 is a bit pattern of our choosing, which in our example was 0x0000. This is loaded into the register in positions 15 through 0, resulting in the pattern 0x0000000000000000 (red nibbles are the imm16 value).
2. The entire pattern is then NOT’d to produce
3. 0xFFFFFFFFFFFFFFFF = -1.

---
MOV vs MOVN: N is for NOT
1. Important note:
3. N, for NOT, is not the same as two’s complement negation. Two’s complement negation requires NOTing a bit pattern, and then adding 1. Here we only NOT’d a bit pattern.

---
Another Approach
1. We could have used a different approach, but using two instructions:
  1. MOV X0, #1
  2. SUB X0, XZR, X0
4. This instruction (SUB) subtracts 1 from the zero register (a register that always contains zero only). The instruction NEG Xd Xr is an alias of SUB Xd, XZR, Xr, meaning both will be assembled to the same machine instruction.

---
Flags

---
Flags and the NZCV register
Aarch64, like many processors, has a special register that contains “flags”, individual bits which represent different results of a previous operation. They are:
- N, negative: the result of the previous flag-setting operation was negative
- Z, zero: the result of the previous flag-setting operation was zero
- C, carry: the result of the previous flag-setting operation involved a final carry (e.g. unsigned integers)
- V, overflow: the result of the previous flag-setting operation involved an overflow (e.g. signed integers)

---
Flag-setting Instructions
1. Example: ADD vs. ADDS
2. ADD Xd, Xr, Xs computes the sum of Xr and Xs. If the result is zero, negative, or involves a carry or overflow, this information is not kept.
4. ADDS Xd, Xr, Xs does the same, but updates the appropriate flag(s) N, Z, C, or V.
6. Using flags allows us to do lots of things!

---
Flag-setting Instructions
1. Example: ADD vs. ADDS
2. ADD Xd, Xr, Xs computes the sum of Xr and Xs. If the result is zero, negative, or involves a carry or overflow, this information is not kept.
4. ADDS Xd, Xr, Xs does the same, but updates the appropriate flag(s) N, Z, C, or V.
6. Using flags allows us to do lots of things!

---
Flag-reading instructions
1. Example: ADC and ADCS
3. ADC Xd, Xr, Xs performs Xr + Xs + C, but does not set flags.
4. ADCS Xd, Xr, XS performs Xr + Xs + C, and does set flags.
6. We could use this to define (for example) addition with 128 bit numbers: future assignment?

---
Flag-reading instructions: branching
AKA: JUMPs on ARM
1. In the Brookshear architecture, we had a single JUMP command, and it was supplied with two operands: the register to compare to R0, and the memory location to jump to. Put another way, JUMP on Brookshear was “branch on equality.”
3. ARM has way more variations on this type of instruction (fortunately).

---
Branching
1. The most basic instruction is an unconditional branch, which has assembly code B. Its syntax would be
3. B <label>
5. where <label> is (eventually) an address. In assembly this is a label like main: or chocolate: but eventually is resolved to a memory address.

---
Branching
1. Another branch instruction is
3. BR Xr
5. Here the program counter is set unconditionally to have the value stored in Xr, which is interpreted as a memory address.

---
Branching
1. A more exotic one is
3. B.cond <label>
5. Here cond refers to a condition, which can have 16 possible values/meanings, and branching is conditional on the value(s) of the NZCV flags.

---
Branching
1. A few of the codes:
3. EQ: branch on equal
4. NE: branch on not-equal
5. GE: greater than or equal
6. GT: greater
7. etc.
9. Generally we use a CMP instruction before a B.cond instruction.

---
CMP
1. CMP neesd to be specified two registers for comparison, Rm and Rn (either W or X):
2. CMP X0, X1.
3. This really is an alias for
4. SUBS Xzr X0 X1, which computes X0-X1, discards the result but updates the flags. The flags can then be read by a branch instruction immediately following the comparison.
6. There are “options” that can be added to make the CMP function a bit more elaborate, but we’ll skip that for now.

---
CBZ/CBNZ
1. These instructions have format
2. CBZ/CBNZ Rs, <label>
3. Unlike the other compare commands, they do not change the flags and are in a sense a CMP + B put together into a single instruction.
5. CBZ and CBNZ genuinely a single instruction and have different op codes than the CMP command: they are not an alias for CMP + B.cond.