Byte-level work
1. We have the LDR command, that loads a register with the contents starting at a given memory address: either 4 byres for a W register, or 8 bytes for an X register.
3. But as we’ve seen with strings, each character is stored as a single byte (in ASCII), and we’d need a way to load a single byte into a register if we wanted to process textual data.

---
1. Solution? RTFM. There are more op-codes similar to LDR but that work on smaller units of data:
3. Byte: LDRB Wr, [addr]
4. Half-word (two bytes): LDRH Wr, [addr]
5. Word (four bytes) LDR Wr, [addr]
6. Double word: LDR Xr, [addr]
8. Similar modifications for STR.

---
1. Example: let’s write a program to accept a string from the user, then calculate the length of the string by looking for the null terminator.
3. We’ll write a main routine and a subroutine called scanstr. scanstr will accept a memory location (in X0) as input, start scanning there, and output (in X0) the length of the string. It’ll use a loop, and will stop when it hits the null terminator. We’ll use X1 as a counter/offsetter, which will initially start at 0.